## Slide 1: NVM Read Me

## Slide 2
NVM Guide
Potential NVM’s to choose from:
1. I217–LPT-H*(A3)-16 Flex Filters, No Ultra Low Power(ULP) support
2. I218–LPT-LP**(B1)- ULP support with 16 Flex Filters
3. I218–LPT-H*(Refresh/B1)– 16 Flex Filters, No ULP support
4. I218–WPT-LP***(B1)– ULP, 16 Flex Filters, Connected Standby (CS) support, c9/c10
5. I219-SPT-LP (A0) – 32 Flex Filters, ULP, CS, c9/c10 support
6. I219-SPT-H (A0) – 32 Flex Filters, ULP, CS, c9/c10 support
7. I219-KBL-LP (A0) – 32 Flex Filters, ULP, CS, c9/c10 support
8. I219-KBL-H (A0) – 32 Flex Filters, ULP, CS, c9/c10 support
9. I219-LBG/Purley – 32 Flex Filters, ULP support

## Slide 3
NVM Guide
#2 through #4 NVM’s Provided in SVK SW5 Release:
  2 (Device ID: LM=155A, V=1559), 3 (Device ID: LM=15A0, V=15A1), and
  4 (Device ID: LM=15A2, V=15A3) only
  **LPT-LP=Lynx Point-Low Power, ***Wildcat Point-Low Power
#5 through #6 NVM’s Provided in I219 PV VIP Release:
  ****SPT-LP=Sun Rise Point-Low Power, SPT-H
  5 (Device ID: LM=156F, V=1570), 6 (Device ID: LM=15B7, V=15B8)
#7 through #8 NVM’s Provided in I219 SW3 Kabylake DT & MB VIP Kit Release:
  *****KBL-LP=Kabylake-Low Power, KBL-H
  7 (Device ID: LM=15D7, V=15D8), 8 (Device ID: LM=15E3, V=15D6)
#9 NVM’s Provided in I219 SW3 Purley Package VIP Kit Release:
  ******LBG/Purley=Lewisburg/Purley
  9 (Device ID: LM=15B9, V=15BA)

## Slide 4
NVM | Platform | CPU | PCH | 
LPT-H Desktop (Lynx Point/I217) | Shark Bay | Haswell | Lynx Point Example: Q87, H87, Z87, B85, H81, QM87, HM87 | 
LPT-LP Mobile (Lynx Point/I218) | Shark Bay Mobile | Haswell-U/ Y | Lynx Point | 
LPT-H Desktop (Lynx Point/I218) | Shark Bay Refresh | Haswell | Lynx Point Example: Z97, H97 | 
LPT-H Desktop/Servers (Lynx Point/I218) | Grantley and X99 | Haswell-EP | Lynx Point Example: C226, C224, C222, X99 | 
LPT-H Desktop/Servers (Lynx Point/I218) | Grantley and X99 Refresh | Broadwell-EP | Lynx Point Example: C226, C224, C222, X99 | 
WPT Mobile (Wildcat Point/I218) | Broadwell Mobile | Broadwell-U/ Y | Wildcat Point | 
SPT-LP Mobile (Sunrise point/I219) | Skylake Mobile | Skylake-U/ Y | Sunrise Point | 
SPT-H Desktop/Servers (Sunrise Point/I219) | Skylake | Skylake-S/ H Kabylake-S /H | Sunrise Point Example: Q170, Z170, H170, H110, B150, C236, C232 | 
KBL-LP Mobile (Kabylake I219) | Kabylake Mobile | Kabylake-U/ Y | Sunrise Point | 
KBL-H Desktop/Servers (Kabylake I219) | Kabylake | Skylake-S/ H Kabylake-S/ H | KBP-H | 
LBG Servers (Purley/I219) | Purley | Skylake | Lewisburg | 

## Slide 5
LOM | Device ID
82579-LM | 0x1502
82579-V | 0x1503
I217-LM | 0x153A
I217-V | 0x153B
I218-LP-LM | 0x155A
I218-LP-V | 0x1559
I218-LPT-H-LM | 0x15A0
I218-LPT-H-V | 0x15A1
I218WPT-LP-LM | 0x15A2
I218WPT-LP-V | 0x15A3
I217 & I218 Device ID Quick Reference Guide

## Slide 6
I219 Device ID Quick Reference Guide
Platform | I219 | Device ID
SkyLake Y/U | SPT-LP-I219-LM | 0x156F
 | SPT-LP-I219-V | 0x1570
SkyLake S/ H; Greenlow (SkyLake workstation platform) | SPT-H-I219-LM | 0x15B7
 | SPT-H-I219-V | 0x15B8
KabyLake Y/U | KBL-LP-I219-LM | 0x15D7
 | KBL-LP-I219-V | 0x15D8
KabyLake S/ H | KBL -H-I219-LM | 0x15E3
 | KBL -H-I219-V | 0x15D6
Purely | LBG-I219-LM | 0x15B9
 | LBG-I219-V | 0x15BA